## Slide 1: Traxxas Slash 4x4 Vxl
ME49601 TOOLS/METHODS FOR ITERATIVE PRODUCT DESIGN & ANALYSES
Team Trophy Truck
Jonathan Jackson, Connor Day, Sidh Gurnani, William Snyder
School of Mechanical Engineering, Purdue University

## Slide 2: Outline
Team Organization and Collaboration
  File Structures
  Team organization
  Roles and Responsibilities
CAD Overview
  CAD structure
  Wireframe and Shared Parameters
  Surface and Solid Modeling
  Mass Properties
Analysis
  Component and Assembly FEA
  Topology Optimization
  CFD
Visualization

## Slide 3: Team Organization and Communication

## Slide 4: Team Organization and Communication
File Structures
OneDrive Shared folder with all files
Files transfer to other softwares:
  FEA  STEP files
  CFD  Parasolid Files

## Slide 5: Team Organization and Communication
Team Organization
Item Checklist
  Helped with accountability and progress tracking
Schedule to keep all deadlines and relevant information in one place
Text Group chat for easy communication
Parts List and BOM:
  Helps keep track of parts and also ensures the team doesn’t overlook parts during CAD and Analysis
  Not all hardware is included in BOM, but instructions on where to keep hardware are provided
Team Standards:
  Standardization of units, naming conventions
  Text Group chat with reminders

## Slide 6: Team Organization and Communication
Roles and Responsibilities
Name | Responsibility
Jonathan Jackson | Chassis
Connor Day | Drivetrain/FEA & Topology
Sidh Gurnani | Primary Shell Surface/CFD
William Snyder | Front/Rear Suspension

## Slide 7: CAD Overview

## Slide 8: CAD Overview
CAD Structure
Top-Down Skeleton
Overall System Geometry
Subsystems
Shell
Expressions
Drivetrain
Chassis
Suspension

## Slide 9: Overall CAD

## Slide 10: CAD Overview
Wireframe and Shared Parameters
Global Scale Factor
Accurate Datum Planes/Wireframe model for sub-assembly references
Relevant geometry from skeleton and wireframes wavelinked into parts and assemblies as needed
Linked parameters were also used to share dimensions

## Slide 11: CAD Overview
Primary Surface Modeling

## Slide 12: CAD Overview
Slightly modified from Traxxas’s
  Overall tighter packaging and reduction of sharp corners throughout surface
  Creates smoother surface overall
Primary Surface Modeling

## Slide 13: CAD Overview
Secondary Surface Modeling

## Slide 14: CAD Overview
Solid Modeling: Suspension Subassemblies
Select parts were modeled with Optimization in mind

## Slide 15: CAD Overview
Solid Modeling: Suspension Re-Engineering
Rear suspension had no upper supports
Rear suspension location change

## Slide 16: CAD Overview
Solid Modeling: Chassis
Modeled with optimization in mind
More time for finer details
Integrate with front & rear suspension

## Slide 17: CAD Overview
Mass Properties
Mostly ABS Plastic (high impact in Ansys)
  Shell is Polycarbonate
Yield Strength: 40 ksi
Differs in CAD because of lack of optimized parts and design improvements

## Slide 18: Analysis and Optimization

## Slide 19: Analysis and Optimization
Chassis Torsion and Impact FEA
Fixed back plane
Cylindrical Supports at bolt holes
Tetrahedral Mesh size: .25”
Moment applied at front face
Torsional stiffness provides basis for future assembly FEA and validates rigid constraints. Low deflection shows this is strong enough to assume this.

## Slide 20: Analysis and Optimization
Chassis Side Impact FEA
Same setup as previous
50lbs on leftmost edge upward
Stress is high but not close to 2.0 FOS

## Slide 21: Analysis and Optimization
Chassis Front Impact FEA
Same Fixed Geometry
500lbf applied at front face
Low stress allows for much material removal

## Slide 22: Analysis and Optimization
Chassis Topology Optimization
Kept outside geometry
Fixed back face
20% weight reduction and 1.3 stiffness factor
Force applied at front edge to simulate front impact, putting chassis in bending
Significant amount of material can be removed
Study 1
Study 2

## Slide 23: Analysis and Optimization
Drivetrain FEA Torque Calcs
Motor Data:
Titan 12T
Max Torque Output: 1.5-2Nm
Gear Ratio: 3.57:1
Pressure Angle: 20 deg.
Torque at Gear: 63.216 in-lbs
Equivalent Force Tangent = 75.708 lbs
Equivalent Force at Pressure angle: 208.005 lbs

## Slide 24: Analysis and Optimization
Drive Gear FEA
Tetrahedral Mesh (size .035 in)
ABS plastic (high impact)
Torque applied from calculation: 63.2 in-lbs at center cylinder
Fixed cylindrical supports at bolts and at edge
Material Yield: 36 ksi

## Slide 25: Analysis and Optimization
Driveshaft FEA
3D Tet Mesh
Fixed Constraint
Applied Torque
Result

## Slide 26: Analysis and Optimization
Bottom Support Topology Optimization
Cylindrical Supports at bolt holes and bearing
Keep Geometry outline
Forces applied at outer cylinder and shock mount point
20% weight reduction and 1.2 deflection factor
Would need to keep material in center for additional stiffness

## Slide 27: Analysis and Optimization
Suspension Center Piece Topology Optimization
Fixed geometry
100 lb applied at 30 degrees

## Slide 28: Analysis and Optimization
Wheel Attachment Topology Optimization
Manufacturing constraints on holes for bolts and wheel
Fixed geometry at outer boundaries
Force Applied at the Wheel Center Inboard
10% weight reduction and 1.1 deflection factor

## Slide 29: Analysis and Optimization
Front Bumper FEA
Cylindrical Supports at bolts and posts
Force applied as shown
Tetrahedral Mesh Size: .1”

## Slide 30: Analysis and Optimization
Rear Bumper FEA
Cylindrical Supports at bolt holes, all fixed
Tetrahedral Mesh size: .1”
Force applied: 50 lbf

## Slide 31: CFD

## Slide 32: CFD
Shell CFD
Mock wind tunnel created in CAD
Meshers: Surface Remesher, Trimmed Cell Mesher, Prism Layer Mesher
Element Size: 0.025m
Prism Layer Total Thickness: 10% (of base size)
Physics Model Selection: Gas, Segregated Flow, Ideal Gas, Segregated Fluid Temperature, Steady, Turbulent, K-Epsilon Turbulence
Test Cases: 36 mph, 45 mph, 70 mph, 100 mph

## Slide 33: CFD
36 mph – Scalar Scene

## Slide 34: CFD
36 mph – Vector Scene

## Slide 35: CFD
36 mph – Drag Force Plot

## Slide 36: CFD
45 mph – Scalar Scene

## Slide 37: CFD
45 mph – Vector Scene

## Slide 38: CFD
45 mph – Drag Force Plot

## Slide 39: CFD
70 mph – Scalar Scene

## Slide 40: CFD
70 mph – Vector Scene

## Slide 41: CFD
70 mph – Drag Force Plot

## Slide 42: CFD
100 mph – Scalar Scene

## Slide 43: CFD
100 mph – Vector Scene

## Slide 44: CFD
100 mph – Drag Force Plot

## Slide 45: CFD
Drag Force at 300th Iteration
Drag Increases as speed goes up in expected manner
Therefore, methodology conducted for CFD is valid and these results can be used to draw some conclusions
Case | Force (N)
36 mph | 3 N
45 mph | 4.75 N
70 mph | 10.8 N
100 mph | 22 N

## Slide 46: Visualization

## Slide 47: Visualization
Full Assembly Visualization

## Slide 48: Visualization
Full Assembly Visualization

## Slide 49: Visualization
Full Assembly Visualization

## Slide 50: Visualization
Full Assembly Visualization

## Slide 51: Part Visualization
Suspension Assembly Visualization

## Slide 52: Part Visualization
Shell Visualization

## Slide 53: Improvements, Successes, and Difficulties
What we did well:
Thorough FEA, CFD, and Topology Optimization
Unaltered CAD for optimization later
Communication
Organization
Future Improvements:
Focused on optimizing wide range of parts, did not have time to implement them into CAD
Phase out OneDrive (not good for CAD structures and file sharing) for Teamcenter, etc.
More robust scaling factor
More CFD at different angles
  Rear wing addition, other technical improvements
Difficulties
Version control for CAD parts and assemblies
Breaking or replacing references when files moved for organizational purposes or scaled
File sharing system made development slower
Scaling factor, when changed, would randomly break some constraints in assemblies
Difficult time constraints prevented implementation of optimized parts into assembly for accurate weights

## Slide 54: Thank You